## Slide 1: Experiment 5: ALP for Average of N Numbers and Fibonacci Series
Dr. Subhradeep Pal
Department of EEE

## Slide 2
5.1 FIND THE AVERAGE OF N NUMBERS.
5.2 FIND THE FIBONACCI SERIES.
ALPs to be completed

## Slide 3
Objective: To find average of N numbers stored.
Formula:
5.1 Average of N numbers

## Slide 4
org 100h
MOV AX,0000H
MOV SI,xxxxH
MOV CX,xxH
MOV DX,xxH
loop: ADD AL,[SI]
INC SI
INC DX
CMP CX,DX
JNZ loop
DIV CL
MOV [xxxxH],AX
HLT
ret
Pseudocode
Values in decimal:
03, 04, 05, 08
Result in decimal: 05
SI register location: 1100H
Result location: 1200H
Note: SI register content is the offset relative to DS. Make sure to load the data in appropriate locations prior to execution of the code.
Change here to complete the code.

## Slide 5
1. What if the accumulator is not initialized to zero ?
2. Does it have any effect on output result if the accumulator
is not initialized to zero?
3. Repeat the problem with five numbers of 16-bit data of
your choice. What are changes you had made in your code?
Review Questions

## Slide 6
Each number is the sum of the two preceding ones, starting from 0 and 1 as depicted below.
Fibonacci series
0, 1, 1, 2, 3, 5, 8, 13, 21......
5.2 Fibonacci series

## Slide 7
org 100h
MOV AX,xxH
MOV SI,yyyyH
MOV [zz],AL
INC zz
ADD AL,01H
MOV [SI],AL
MOV CX, [600H]
SUB CX,wwwwH
L1: MOV AL,[zz-1]
ADD AL,[SI]
INC zz
MOV [zz],AL
LOOP L1
HLT
Pseudocode
Change here to complete the code.
Assume SI location to be 500h.
Initialize the AX register to free it from garbage value.

## Slide 8
1. Why is sub instruction used ?
2. What is the replaced number instead of “pp” and why is it so?
3. Which addressing mode is used in this programming?
4. What is the role of LOOP instruction in this ALP?
Review Questions