## Slide 1: Experiment 6: Arranging numbers in ascending order and finding matrix addition for two numbers
Dr. Subhradeep Pal
Department of EEE

## Slide 2
ALPs to be completed
Problem 1: Arrange numbers in ascending order.
Problem 2: Find matrix addition (2 × 2) for two numbers.

## Slide 3
6.1 Arrange numbers in ascending order
Assume the numbers and memory locations are given by
Data | A2h | 23h | 66h | 12h | 7Dh
Add. | 501 | 502 | 503 | 504 | 505
Number of passes required: N-1
Pass1 | A2h | 23h | 66h | 12h | 7Dh
 | 23h | A2h | 66h | 12h | 7Dh
 | 23h | 66h | A2h | 12h | 7Dh
 | 23h | 66h | 12h | A2h | 7Dh
 | 23h | 66h | 12h | 7Dh | A2h
(1 number sorted)

## Slide 4
6.1 Arrange numbers in ascending order
Pass 2 | 23h | 66h | 12h | 7Dh | A2h
 | 23h | 66h | 12h | 7Dh | A2h
(3 numbers sorted)
Pass 3 | 23h | 66h | 12h | 7Dh | A2h
 | 23h | 12h | 66h | 7Dh | A2h
 | 23h | 12h | 66h | 7Dh | A2h
Pass 4 | 23h | 12h | 66h | 7Dh | A2h
 | 12h | 23h | 66h | 7Dh | A2h
(All numbers sorted)
(2 numbers sorted)

## Slide 5
6.1 Arrange numbers in ascending order
org 100h
MOV SI, xxxxh
MOV CL, [yy]
DEC CL
L1: MOV SI, xxxxh
MOV CH, [yy]
DEC CH
INC SI
L2: MOV AL, [yy]
INC SI
CMP AL, [yy]
JC L3
XCHG AL, [yy]
DEC SI
XCHG AL, [yy]
INC SI
L3: DEC CH
JNZ L2
DEC CL
JNZ L1
HLT
ret
Assume SI = 0500h
Change the values of xxxxh and yy
to complete the code.
Pseudocode
Load the following numbers in the exact order:
A2, 23, 66, 12, 7D
Load the number in the RAM prior to execution of your code.

## Slide 6
How CMP instruction works?
Which registers are to be modified for 16-bit data?
Repeat the problem using the data in the following order:
99H,12H,56H,45H,36H
4. What should be the content of the memory location
0700:0500?
6.1 Review Questions

## Slide 7
6.2 Matrix addition (3 × 3) for two numbers
Matrix to be stored in the form of array in the memory location.
Storing matrix data to be taken care by BX, BP and DI registers.
SI to be used to identify the data locations.
Arithmetic operation to be done element wise.
Loop instruction to be used to repeat the operations
CL register to store the number of data in a matrix.
+
Matrix 1
Matrix 2
Matrix 3
1. To be loaded by BX register
2. To be loaded by BP register
3. To be loaded by DI register

## Slide 8
6.2 Matrix addition (3 × 3) for two numbers
org 100h
MOV BX,xxxxH
MOV BP,yyyyH
MOV DI,zzzzH
MOV SI,0001H
MOV CL,wwH
L1: MOV AL,[BX+SI]
ADD AL,[BP+SI]
MOV [zz],AL
INC SI
INC DI
LOOP L1
HLT
ret
Assume: BX = 1300H; BP = 1400H
and DI = 1500H.
Changes are to be made to complete the ALP.
Pseudocode

## Slide 9
What should be the value of CL represent in the given pseudocode?
Change the previous code to solve the following.
6.2 Review Questions
+