## Slide 1: Experiment 9: Write a program to control the operation of stepper motor.
Dr. Subhradeep Pal
Department of EEE

## Slide 2
Write a program to control the operation of stepper motor in clockwise direction.
Write a program to control the operation of stepper motor in anti-clockwise direction.
ALPs to be completed

## Slide 3
9.1 Stepper Motor in Emulator
What is a Stepper Motor?
An electric motor that can be precisely controlled by signals from a computer.
The motor turns through a precise angle each time it receives a signal.
By varying the rate at which signal pulses are produced, the motor can be run at different speeds or turned through an exact angle and then stopped.
This is a basic 3-phase stepper motor, it has 3 magnets controlled by bits 0, 1 and 2. other bits (3..7) are unused.
When magnet is working it becomes red. The arrow in the left upper corner shows the direction of the last motor move. Green line is here just to see that it is really rotating.

## Slide 4
9.1 Stepper Motor in Emulator
Port Address: 07H
Instruction to include stepper motor in emulator:
#start=stepper_motor.exe#
How to test the virtual stepper motor is ready or not?
Test the bit pattern 1000 0000b with AL. If ready, the MSB will be 1.
or else it will not.
How to load data in Stepper motor?
Use IN and OUT instruction. For out instruction select port 7

## Slide 5
9.1 Stepper Motor in Emulator
How to choose data for clockwise rotation?
How to choose data for anti-clockwise rotation?
Bit 1 | Bit 2 | Bit 3 | Bit 4 | Final Data
0 | 0 | 1 | 1 | 0000_0011
0 | 1 | 1 | 0 | 0000_0110
1 | 1 | 0 | 0 | 0000_1100
1 | 0 | 0 | 1 | 0000_1001
Bit 1 | Bit 2 | Bit 3 | Bit 4 | Final Data
1 | 0 | 0 | 1 | 0000_1001
1 | 1 | 0 | 0 | 0000_1100
0 | 1 | 1 | 0 | 0000_0110
0 | 0 | 1 | 1 | 0000_0011

## Slide 6
9.1 Stepper Motor Operation
ALP for clockwise rotation (2-Phase Operation)
#start=stepper_motor.exe#
jmp start
datain db 0000_0011b
db 0000_0110b
db 0000_1100b
db 0000_1001b
START: MOV BX, offset datain
MOV SI,0h
NEXT_STEP:
WAIT: IN AL,07H
TEST AL,10000000b
JZ WAIT
MOV AL,[BX][SI]
OUT 7,AL
INC SI
CMP SI,4
JC NEXT_STEP
MOV SI,0
JMP NEXT_STEP
Initializes the virtual stepper motor
Data for clockwise rotation (8-bit format)
Calculates the offset of the initialized data
Tests if the stepper motor ready or not
Loads the first data in AL
Loads the default content of stepper motor
Loads the data into stepper motor
Increase SI for next data
Compare the value of SI with 4 data in ‘datain’. If equal load 0 to SI and keep the loop running. If not equal complete the operation for first 4 data.

## Slide 7
9.2 Stepper Motor Operation
ALP for anti-clockwise rotation (2-Phase Operation)
#start=stepper_motor.exe#
jmp start
datain db 0000_xxxxb
db 0000_xxxxb
db 0000_xxxxb
db 0000_xxxxb
START: MOV BX, offset datain
MOV SI,0h
NEXT_STEP:
WAIT: IN AL,07H
TEST AL,10000000b
JZ WAIT
MOV AL,[BX][SI]
OUT 7,AL
INC SI
CMP SI,4
JC NEXT_STEP
MOV SI,0
JMP NEXT_STEP
Initializes the virtual stepper motor
Data for anti-clockwise rotation (8-bit format). Change here.
Calculates the offset of the initialized data
Tests if the stepper motor ready or not
Loads the first data in AL
Loads the default content of stepper motor
Loads the data in stepper motor
Increase SI for next data
Compare the value of SI with 4 data in ‘datain’. If equal load 0 to SI and keep the loop running. If not equal complete the operation for first 4 data.

## Slide 8
Review Questions
What will be the change in ‘datain’ for the clockwise rotation for half step-rotation in the stepper motor? Show your answer by changing the ALP.
Repeat the previous problem for anticlockwise direction.
What is the difference between half-step and full-step rotation in stepper motor?
Which IC is used to interface a stepper motor and 8086 in real-life scenarios?