## Slide 1: Experiment 11: Write a program to display numbers in LED based display.
Dr. Subhradeep Pal
Department of EEE

## Slide 2
Write a program to display a number using 8086 and a virtual LED based display.
ALPs to be completed

## Slide 3
LED Display in Emulator
A LED display is available in EMU8086 with port address 199.
It consists of 5 LED based display which can be used to show a number (both positive and negative).
The display number can be provided using any 8086 ALP or using a simple loop.
Port Address
Display number using LED array

## Slide 4
LED Display in Emulator
Port Address: 199
Instruction to include stepper motor in emulator:
#start=led_display.exe#
How to load the control word in traffic light?
Use OUT instruction. For out instruction select port 199. Use AX
register to store hexadecimal word intermediately.

## Slide 5
ALP for LED based Display
#start=led_display.exe#
#make_bin#
name "led"
mov ax,0
out 199,ax
mov ax, zzzzz
out 199, ax
mov ax, vwxyz
out 199, ax
; Eternal loop to write
; values to port:
mov ax, yy
x1:
out 199, yy
inc zz
jmp yy
hlt
Initializes the virtual LED display
Store an arbitrary positive number in AX and send it IO
Load 0 in the display
Start from 0. Each step increases one value and load the updated number in the LED display. Continue to increase the value.
Store an arbitrary negative number in AX and send it IO
Initialize AX by 0.
Concept of #make_bin#
A simple executable file.
You can define the values of all registers, segment and offset for memory area where this file will be loaded.
When loading "MY.BIN" file to emulator it will look for a "MY.BINF" file, and load "MY.BIN" file to location specified in "MY.BINF" file, registers are also set using information in that file.
In case the emulator is not able to find "MY.BINF" file, current register values are used and "MY.BIN" file is loaded at current CS:IP and the execution starts from the current value of CS:IP.
Bin file type is not unique to the emulator, however the directives are unique and will not work if .bin file is executed outside of the emulator because their output is stored in a separate file independently from pure binary code.

## Slide 6
Review Questions
Write an ALP which will display integer values from -5 to +5 using the virtual LED segment display. Use JL instruction for jump.